## Slide 1: ARDUINO MASTER CLASS
21
Keypad with Arduino

## Slide 2: 21 AGENDA 01 02 03
Keypad
Interview questions &Tech News
Interface Keypad witch Arduino

## Slide 3: Keypad
Each switch in a row is connected to the other switches in the row by a conductive trace underneath the pad.
Each switch in a column is connected the same way – one side of the switch is connected to all of the other switches in that column by a conductive trace.
Each row and column is brought out to a single pin, for a total of 8 pins on a 4X4 keypad:

## Slide 4: Keypad Working

## Slide 5: Keypad with Arduino

## Slide 6: 16x2 LCD with Arduino using I2C

## Slide 7: INTERVIEW QUESTIONS What is a Filter Ripple Carry Adder and Carry Look Ahead Adder SCR
In ripple carry adder, the carry bits ripple through each individual adder while in a carry-look-ahead adder, the carry bit is determined separately using a CLA (Carry look ahead) block.
A Filter is an electronic circuit that removes specific or unwanted frequency components from a signal.
Low pass filter
Bandpass filter
Band stop or band reject filter
High pass filter
Notch filter
Silicon controlled rectifier is unidirectional semiconductor machine, but unlike diode, it has three terminals Anode, Cathode & Gate. The SCR can be switched on & off using the entrance input.

## Slide 8: THANKS!